## Slide 1: INTRODUCTION TO DEVICE DRIVERS
Tuba Yavuz
EEL 4930/5934 Advanced Systems Programming
University of Florida

## Slide 2: Outline
Device driver entry points
Code walkthrough
Compiling a device driver
(Un)loading a device driver
Using the module

## Slide 3: Entry points
f_op
owner
open
release
read
write
f_op
struct file
struct cdev
struct file_operations
static int mycdrv_open()
static int mycdrv_release()
static ssize_t mycdrv_read(…)
static ssize_t mycdrv_write(…)
static int __init mycdrv_init(void)
static int __exit mycdrv_exit(void)
MODULE for the DRIVER
adds
/dev/mycdrv
deletes
Major
Minor1
Minor2
…
Minork
Device
Number
Region
registers
initializes
*collection of function pointers*,
Every open file has one
*represents an open file*
Created on open, deleted when all instances of file closed
Has pointer to
Kernel uses this to
Represent Char devices
internally
Has pointer to
Notes: blalbalbalb

## Slide 4: Variable declarations
#define MYDEV_NAME "mycdrv"
static char *ramdisk;
#define ramdisk_size (size_t) (16*PAGE_SIZE)
static dev_t first;
static unsigned int count = 1;
static int my_major = 700, my_minor = 0;
static struct cdev *my_cdev;
static const struct file_operations mycdrv_fops = {
.owner = THIS_MODULE,
.read = mycdrv_read,
.write = mycdrv_write,
.open = mycdrv_open,
.release = mycdrv_release,
};

## Slide 5: init function
static int __init my_init(void)
{
ramdisk = kmalloc(ramdisk_size, GFP_KERNEL);
first = MKDEV(my_major, my_minor);
register_chrdev_region(first, count, MYDEV_NAME);
my_cdev = cdev_alloc();
cdev_init(my_cdev, &mycdrv_fops);
cdev_add(my_cdev, first, count);
pr_info("\nSucceeded in registering character device %s\n", MYDEV_NAME);
return 0;
}
module_init(my_init);

## Slide 6: exit function
static void __exit my_exit(void)
{
cdev_del(my_cdev);
unregister_chrdev_region(first, count);
pr_info("\ndevice unregistered\n");
kfree(ramdisk);
}
module_exit(my_exit);

## Slide 7: open and release functions
static int mycdrv_open(struct inode *inode, struct file *file)
{
pr_info(" OPENING device: %s:\n\n", MYDEV_NAME);
return 0;
}
static int mycdrv_release(struct inode *inode, struct file *file)
{
pr_info(" CLOSING device: %s:\n\n", MYDEV_NAME);
return 0;
}

## Slide 8: read function
static ssize_t
mycdrv_read(struct file *file, char __user * buf, size_t lbuf, loff_t * ppos)
{
int nbytes;
if ((lbuf + *ppos) > ramdisk_size) {
pr_info("trying to read past end of device,"
"aborting because this is just a stub!\n");
return 0;
}
nbytes = lbuf - copy_to_user(buf, ramdisk + *ppos, lbuf);
*ppos += nbytes;
pr_info("\n READING function, nbytes=%d, pos=%d\n", nbytes, (int)*ppos);
return nbytes;
}

## Slide 9: write function
static ssize_t
mycdrv_write(struct file *file, const char __user * buf, size_t lbuf,
loff_t * ppos)
{
int nbytes;
if ((lbuf + *ppos) > ramdisk_size) {
pr_info("trying to read past end of device,"
"aborting because this is just a stub!\n");
return 0;
}
nbytes = lbuf - copy_from_user(ramdisk + *ppos, buf, lbuf);
*ppos += nbytes;
pr_info("\n WRITING function, nbytes=%d, pos=%d\n", nbytes, (int)*ppos);
return nbytes;
}

## Slide 10: Compiling the module
Sample Makefile for compiling the device driver:
obj-m += sample_driver.o
Store the Makefile in the same directory as sample_driver.c is
and in that directory do
$ make –C<path to kernel source> M=$PWD modules
-C: changes the directory to the kernel source directory and
uses the top Makefile.
M: Makes the Makefile move back to the module source
directory before building the modules target.

## Slide 11: (Un)loading a device driver
To load a device driver module:
$ insmod sample_driver.ko
To unload a device driver module
$ rmmod sample_driver

## Slide 12: Using the module
Create the device node!
$mknod /dev/mycdrv c 700 0
(Assuming module is loaded) Use the module
$ echo Hello Device > /dev/mycdrv
$ cat myfile.txt > /dev/mycdrv
$ dd if=/dev/zero of=/dev/mycdrv count=1
$ dd if=/dev/mycdrv count=1